## Slide 1
DrEyeVer
Detecting object on driver’s focus of attention for intelligent vehicles.
Team KaAI
Kookmin Univ.
South Korea
2020. 10. 02

## Slide 2
Contents
  Outline
  Background
  Concept
  System Configuration Map (UC_win/Road World)
  Getting Can data from Driving Simulator
  Object Detection from Eye_Tracker Data
  Gaze Point Transfomation to UC_win/Road Screen(1)(2)
  Demo Scenario (UC_win/Road World)
  Applying Eye 4 Vehicles in Real World
  System Configuration Map (Real World)
  Demo Scenario (Real World)

## Slide 3
Background
∙ Not possible to determine if the driver is aware of abnormal vehicles or other road hazards.
  Background
∙ ADAS does not know where the driver’s attention is being focused.
∙ Unnecessary warnings may sound even if the driver has already detected and prepared for the hazard.
∙ If the driver assistance system has information about the driver's focus of attention, it may suppress unnecessary warnings and can more easily detect the driver's intentions and respond to them.

## Slide 4
Concept
In AR environment (Simulator & UC-win/Road)
  Concept
When the driver sees UC-win/Road program in the driving simulator, a Bounding Box is projected on the screen. To the eye, the Bounding Box seems flat. However, a Bounding Box is generated in 3D. Therefore, we can implement the environment like Real World.
My phone is ringing!?
That car just cut in!
That bus suddenly stopped!
Soon it's school zone.
Watch out!
There is a dog on the road!

## Slide 5
System Configuration Map
In AR environment (Simulator & UC-win/Road)
  Map
UC-Win/Road
user
Tobii glasses2
Eye tracker
Perspective Transform
socket communi-cation
Logitech
Manipulator
kvaser leaf light v2
Can USB interface
socket communi-cation
Manipulator
Manipulator
Manipulator

## Slide 6
Getting Can Data from Driving Simulator
  Map
Step 1.
Connect CAN Bus line with Kvaser_leaf_light
Step 2.
Send CAN data(handle angle) to UC-win/Road through TCP/IP
System Configuration Map

## Slide 7
Object Detection from Eye_Tracker Data
  Deep Learning
System Configuration Map
Step 1.
Record Eye_tracker set, for deep Learning
Step 2.
Transforming gaze_point to Virtual world
Step 3.
Labeling objects for object detection(Darknet)
Step 4.
Building a Deep Learning model(Darknet)

## Slide 8
  Gaze Point
System Configuration Map
Step 1.
Get Gaze_point with Tobii Glasses 2
Step 2.
Perspective Transfrom
Step 3.
To UC-win/Road (Socket communication)
Step 4.
Draw Bounding Box or “Warning” Sign
Gaze Point Transformation to UC-win/Road Screen(1)
In AR environment (Simulator & UC-win/Road)

## Slide 9
Gaze Point Transformation to UC-win/Road Screen(2)
In AR environment (Simulator & UC-win/Road)
  Gaze Point
The Gaze point is marked with a red dot in the UC-win/Road program. And when the Gaze point is on the vehicle, a yellow 3D Binding box is created. As a result, we can visually check which vehicle the driver is looking.

## Slide 10
Demo Scenario (UC-win/Road World)
  Simulate
The user just go forward
The user change the lane
Another Car intercepted the user’s line
Complex Situation

## Slide 11
Applying Eyes 4 Vehicles in Real World.
In Real World ( EyeTracker & Camera & Lidar / Sensor )
  Theory
1. Camera costs less but has no depth information which leads to 2D object recognition. On the other hand, lidar with great performance and many layers costs alot.
2. So we complemented both camera and lidar to effectively increase recognition accuracy.
3. We used the real-time coordinates of the eye-tracker to figure out which of the objects the driver is looking, among the objects that the lidar and the camera detected.
4. If the driver is not looking at an object related to a particular hazard situation, a warning is given by sound or visual alert system.
5. This system reduces the driver's risk and prevents accidents.
Applying Eyes 4 Vehicles in Real World.
Lidar Point Cloud
(3D)
360º camera
screen (2D)
Eye Tracker Vector
Driver’s sight

## Slide 12
Applying Eyes 4 Vehicles in Real World.
In Real World ( EyeTracker & Camera & Lidar / Sensor )
  Map
sensor
VLP 16
Three Lidar Calibration
V.360
360-degree camera
Mobileye
ADAS System
Niro
user
Tobii glasses 2
Eye Tracker
Kvaser leaf light v2
Can USB Interface
We can detect objects with our sensor.
With eyeTracker we can support driver ergonomically.
Based on our data collected by our sensors, we can do research on deep learning.

## Slide 13
Demo Scenario (Real World)
  Simulate
The user turns right
The user makes a U-turn.
The car in front suddenly interrupted.
Waiting for a green at an intersection
The user turns left

## Slide 14
Thank you very much for your attention.

## Slide 15
Imaage_opencv.cpp get_qrcode_touch_gazepoint()
Wrapperspectivetransform()
G_monitor==4
Demo.c draw_detection_cv_v3()
Detector.c run_detector()
Darknet.c main()
Demo.c demo()
Getperspectivetransform()
Aruco::detectmarkers()

## Slide 16
Controller.py
Start_recording()
Start_calibration()
Calibrate_and_record.py
Start_streaming()
Python
연결 정상인지?
No_cali
No_streaming